## Slide 1
Message structure
Handbrake request
Reserved for future use
1bit
7bit
Other commands
Turn request: Ranges from 0 to 255. 0 = Turn Left all the way. 127 = Neutral turn. 255 = Turn Right all the way.
Acceleration request: Ranges from 0 to 255. 0 = Accelerate backward 100%. 127 = Idle. 255 = Accelerate forward 100%.
Handbrake request: It can be 0 or 1. 0 = handbrake not requested. 1= handbrake requested.
Camera rotation request: If looking forward is considered 0deg then: 0 = rotate to the left 90deg, 127 = look forward, 255 = rotate to the right 90deg. Any number is valid and usable between 0 and 255.
Turn request
Acceleration request
Camera rotation request
1byte
1byte
1byte
Other commands
1byte
Observation for the above mentioned commands: Any number is valid and usable between 0 and 255.